## Slide 1: PIC – ch. 2c

## Slide 2: 2.5 PIC Data formats
Numbers can be
  Hex
  Binary
  Decimal
  ASCII formats

## Slide 3
4 ways to show HEX numbers –
  34h, 23H
  0x23, 0X34
  Nothing, just the value: 23, 45
  h‘45’
    E4h – x 0E4h – ok!
    0F – ok! 0F = 0Fh

## Slide 4
B’01010011’
b’01010011’

## Slide 5
D’45’
d’56’
.67

## Slide 6: ASCII character
A’2’
A’9’
To define ASCII strings [more than one character], use DB (define byte) directive.

## Slide 7
EQU – equate
EQU  To assign
  fixed data
  SFR address [SFR – special-function reg.] & GPR
  COUNT EQU 0x25
  … …
  MOVLW COUNT ;WREG = 25h

## Slide 8
ORG – origin
ODG directive is used to indicate the beginning of the address.
ORG must be in hex

## Slide 9
END directive
Last line of the PIC program.

## Slide 10
#include
Tells the assembler to use the libraries…

## Slide 11
radix directive
  To indicate the numbering system
    Hex? – by default
    Decimal?
    radix dec
    Numbers will be considered as decimal

## Slide 12
Label:
  1st character must be an alphabetic char.
  1st char – NOT number
  …

## Slide 13: 2.7 PIC prog – assembling & linking
Source file - *.asm
ASM file is fed to the PIC assembler
  It converts codes into machine code
  Produce object file - *.o, error file *.err

## Slide 14
Linking –
  *.hex file
  List file - *.lst
  Map file - *.map
  Debug file - *.cod
After a successful link – hex file is ready to be burned into the PIC’s program ROM and is downloaded into the PIC Trainers.

## Slide 15: Little endian vs. big endian
LE – Low byte goes to low memory & high byte goes to the high mem. address
E.g., all Intel microprocessors …

## Slide 16: 2.9 RISC
Q. How to increase the processing power of a CPU?
  Increase the clock frequency of the chip.
    Higher the frequency, the more power & dissipation
  Use Harvard architecture – increase the no. of buses to bring more info (code & data)
    PIC18 has Harvard acrchi.
  Change internal architecture of the CPU & use RISC architecture

## Slide 17: RISC or CISC?
RISC – reduced | CISC – complex
RISC processors have fixed instruction size | 1, 2, or even 3 bytes
Large no. of registers – at least 32 reg. Large no. registers can avoid the need for a large stack to store parameters | 
Small instruction set. Less instruc. – difficult for programmers! Large programs. Need more memory – but memory is cheap now! PIC16 has 35 instructions PIC18 has 75 instructions | CISC – Complete/Complex instr. Set computer! - Not all instrc. are used n not often too.!